## Slide 1: REMINGTON 870P SHOTGUN
REMINGTON 870P SHOTGUN

## Slide 2: REMINGTON 870P SHOTGUN
How Many of you are familiar with this Shotgun?
REMINGTON 870P SHOTGUN
Introduced in 1950 by Remington Firearms
Used in the Military and in Combat
It became so popular
  The Peoples Republic of China produced the Shotgun for use in their country under the make of Norinco
  32 Countries currently use the Remington 870 including countries like Iran.

## Slide 3: REMINGTON 870P SHOTGUN
NOMENCLATURE
ALL Parts are Interchangeable
The 870 is a
  Bottom Loading
  Slide Ejecting Receiver
  Tubular Magazine

## Slide 4: REMINGTON 870P SHOTGUN
NOMENCLATURE

## Slide 5: REMINGTON 870P SHOTGUN
Open the Action
Select the Safety
Hold the Fore-End
Press and HOLD the Action Release
Pull the Fore-End DOWN towards the Receiver
The ACTION IS NOW OPEN and the BOLT is to the rear out of VIEW.

## Slide 6: REMINGTON 870P SHOTGUN
Checking the Shotgun prior to Loading
Check the Shotgun to make sure the SAFETY is ON
Look UNDER the Shotgun and Check if you can see the Magazine Tube ORANGE Follower? If so, there no rounds inside the Tube.
If there are rounds inside the Tube, remove them immediately!!!!
Open the ACTION or make sure it is OPEN
Visually and Physically check the CHAMBER for any rounds or obstructions.

## Slide 7: REMINGTON 870P SHOTGUN
Disassembly & Reassembly
Point the Shotgun up in a SAFE direction!!!
Screw and Remove the Magazine CAP
Carefully remove the Barrel and check for obstructions inside the barrel.
Screw the Magazine Cap back on.
Using the Fore-End, move the action to the forward position.
With the Safety on, pull the trigger to test the safety
Safety OFF, place finger on the hole in the bolt and press the trigger. You should feel the firing pin strike your finger.
Reassemble the shotgun, DO NOT OVER tighten the Magazine CAP.

## Slide 8: REMINGTON 870P SHOTGUN
Loading (PATROL READY)
Point the Shotgun up in a SAFE Direction
WATCH and Close the ACTION by moving the Fore-End forward, watch the bolt go forward.
Point the Shotgun in a SAFE Direction and pull the trigger
LOAD (4) Four Less lethal Rounds into the Magazine Tube. Count the rounds as you LOAD them and make SURE they are Less Lethal rounds!!!
Place the Shotgun in the Shotgun Rack in the FRONT of your car.

## Slide 9: REMINGTON 870P SHOTGUN
Unloading a loaded shotgun
Remove the Shotgun from your Vehicle Mount.
Immediately place the SAFETY ON!!!!
Place your 3 fingers and thumb around the Fore-End and your last finger UNDER the Fore-End and WALK the Fore-End downward SLOWLY.
Take your free hand THUMB and push the CARRIER in towards the Bolt and move your thumb up towards the Shell inside the Magazine Tube.
As you walk the Fore-End down, the Less Lethal Round will eject from the magazine tube and you capture it with your thumb and remove it.
Using your left hand thumb, depress the Shell Latch and remove the remaining rounds.

## Slide 10: REMINGTON 870P SHOTGUN
INATTENTION
INATTENTION is the one MAJOR cause of Accidental Discharges in a Shotgun and Rifle.
You’re Loading, Unloading or reloading your Shotgun while talking to somebody else or your mind is thinking of something else besides what your doing.
LOOK and THINK about what you are doing at the time you are doing it.
Do NOT Look around!!!
Do NOT talk to anybody!!!
Look at the rounds you are loading into the Shotgun.

## Slide 11: REMINGTON 870P SHOTGUN
Policy regarding Accidental Discharges
Policy 306.7 States . . . .
Make a VERBAL Report to your Supervisor
If On-Duty, file a written report to your Supervisor
If Off-Duty, file a written report no later then the end of your next regular shift
Unless otherwise directed by a Supervisor

## Slide 12: REMINGTON 870P SHOTGUN
Unloading a Chambered Round
Place the SAFETY ON

## Slide 13: REMINGTON 870P SHOTGUN
Unloading a Chambered Round
Place your 3 fingers and thumb around the Fore-End and your last finger UNDER the Fore-End and WALK the Fore-End downward SLOWLY.

## Slide 14: REMINGTON 870P SHOTGUN
Unloading a Chambered Round
Watch the Ejection Port while you WALK the Fore-End down and wait for the Round to appear.
When the Round appears to be ejecting, remove the round and STOP walking the Fore-End down.

## Slide 15: REMINGTON 870P SHOTGUN
Unloading a Chambered Round
Take your free hand THUMB and push the CARRIER in towards the Bolt and move your thumb up towards the Shell inside the Magazine Tube.
As you walk the Fore-End down, the Less Lethal Round will eject from the magazine tube and you capture it with your thumb and remove it.

## Slide 16: REMINGTON 870P SHOTGUN
Unloading a Chambered Round
Using your left hand thumb, depress the Shell Latch and remove the remaining rounds.
ReLoad your Shotgun ‘Patrol Ready’ and Place it in your vehicle.

## Slide 17: REMINGTON 870P SHOTGUN
QUESTIONS??

## Slide 18: REMINGTON 870P SHOTGUN

## Slide 19: REMINGTON 870P SHOTGUN

## Slide 20: REMINGTON 870P SHOTGUN

## Slide 21: REMINGTON 870P SHOTGUN

## Slide 22: REMINGTON 870P SHOTGUN

## Slide 23: REMINGTON 870P SHOTGUN